## Slide 1
Đỗ Hải Sơn
TRICE: A Channel Estimation Framework for
RIS-Aided Millimeter-Wave MIMO Systems1
1 : K. Ardah, S. Gherekhloo, A. L. F. de Almeida and M. Haardt, "TRICE: A Channel Estimation Framework for RIS-Aided Millimeter-Wave MIMO Systems,“ in IEEE Signal Processing Letters, vol. 28, pp. 513-517, 2021, doi: 10.1109/LSP.2021.3059363.

## Slide 2
Question?
How can we improve efficiency of wireless communication system in 5G and beyond?
  Optimize freq domain efficiency by OFDM (1870).
  Increase the quality of service (QoS): spatial modulation (SM), media-based modulation (MBM), …
  Improve number of UEs at once: Time-Frequency resources (from 4G).
  Antenna array configuration : MIMO, Massive-MIMO, Multi-user Massive-MIMO.
  Can we optimize environment (smart environment) to improve efficiency of wireless communication?
    Reconfigurable intelligent surfaces (RIS) (2018) 2.
2 : C. Liaskos, S. Nie, A. Tsioliaridou, A. Pitsillides, S. Ioannidis and I. Akyildiz, "A New Wireless Communication Paradigm through
Software-Controlled Metasurfaces," in IEEE Communications Magazine, vol. 56, no. 9, pp. 162-169, Sept. 2018.

## Slide 3
Outline
Channel Estimation
RIS-Aided Wireless Communications
Two-Stage RIS-Aided MIMO Channel
Estimation (TRICE)
Conclusion

## Slide 4
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
I. Channel Estimation
Consider a simplest model of channel estimation:
Find h if we known y, x: training base
Find h if we just known about y: blind
Example of MLE estimator (LS method):
h

## Slide 5
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
II. RIS-Aided 3
Metasurface tuned by varactor diodes with vertical and horizontal spacings are smaller than half the wavelength.
Varying the bias voltage from 0 to 19 V is sufficient to modify the phase-shift by at least 180 degrees.
Each elements in RIS turns phase of TX-RIS (beamforming) to optimize value of SNR in RX by Varying the bias voltage.
3 : PEI, Xilong, et al., " RIS-aided wireless communications: Prototyping, adaptive beamforming, and indoor/outdoor field trials., " arXiv preprint arXiv:2103.00534, 2021.

## Slide 6
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
II. RIS-Aided 3
They are built a beamforming codebook for the RIS.
In thier prototype, the phase shifts are quantized to being either or .
Algorithm: set the corresponding bias values on each row or column of RIS with initialize value: homogeneous configuration. Then depending on the Reference Signal Receiving Power (RSRP) at RX, change the matrix reflection coefficients.
3 : PEI, Xilong, et al., " RIS-aided wireless communications: Prototyping, adaptive beamforming, and indoor/outdoor field trials., " arXiv preprint arXiv:2103.00534, 2021.

## Slide 7
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
II. RIS-Aided 3
3 : PEI, Xilong, et al., " RIS-aided wireless communications: Prototyping, adaptive beamforming, and indoor/outdoor field trials., " arXiv preprint arXiv:2103.00534, 2021.
Experimental results: their RIS prototype provides a 26dB power gain compared to the baseline case where the RIS is replaced by a copper plate.
A 27 dB power gain was observed in the short-distance outdoor measurement.

## Slide 8
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
III. Two-Stage RIS-Aided MIMO Channel Estimation (TRICE)
Channel are modeled as Saleh-Valenzuela model4
(1)
4 : A. A. M. Saleh and R. Valenzuela, "A Statistical Model for Indoor Multipath Propagation," in IEEE Journal on Selected Areas in
Communications, vol. 5, no. 2, pp. 128-137, February 1987, doi: 10.1109/JSAC.1987.1146527.

## Slide 9
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
III. Two-Stage RIS-Aided MIMO Channel Estimation (TRICE)
Each block, we need K frames for training process.
Let matrix holding the training vectors of the BS.
Let : matrix holding the phase shift vectors of the RIS.
RIS has h x v elements .
Output of RIS-Aided as follow:
where W, H, Z denote decoding matrix, (), AWGN(0, ).
(2) can re-write as: (3)
By LS method, (3) can solved by: when
In Massive-MIMO: we need a large number of K and long channel coherece-time
4 : A. A. M. Saleh and R. Valenzuela, "A Statistical Model for Indoor Multipath Propagation," in IEEE Journal on Selected Areas in
Communications, vol. 5, no. 2, pp. 128-137, February 1987, doi: 10.1109/JSAC.1987.1146527.

## Slide 10
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
III. Two-Stage RIS-Aided MIMO Channel Estimation (TRICE)
Propose method, from (1):
) = ( ) (4)
From (2): Y = AX + Z (5)
where A = ( ), X = GBQ
and are matrices of 1D steering vector
A is estimated by 2D DOA problem.
Sub-space methods: ESPRIT, MUSIC, … (good performance but high complexity and require a number of samples)
OMP method in compressed sensing techniques: this need .
estimated matrix of A, multipy (5) with
4 : A. A. M. Saleh and R. Valenzuela, "A Statistical Model for Indoor Multipath Propagation," in IEEE Journal on Selected Areas in
Communications, vol. 5, no. 2, pp. 128-137, February 1987, doi: 10.1109/JSAC.1987.1146527.

## Slide 11
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
III. Two-Stage RIS-Aided MIMO Channel Estimation (TRICE)
Exploit by h,v
and are characterized by path azimuth and elevation DOAs (DODs) spatial frequencies at the RIS.
Apply the OMP method to (6), we obtained .
for given , we can compute which is the nth diagonal entry of G
From , , we apply them to (4) to find out .
4 : A. A. M. Saleh and R. Valenzuela, "A Statistical Model for Indoor Multipath Propagation," in IEEE Journal on Selected Areas in
Communications, vol. 5, no. 2, pp. 128-137, February 1987, doi: 10.1109/JSAC.1987.1146527.

## Slide 12
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
III. Two-Stage RIS-Aided MIMO Channel Estimation (TRICE)
4 : A. A. M. Saleh and R. Valenzuela, "A Statistical Model for Indoor Multipath Propagation," in IEEE Journal on Selected Areas in
Communications, vol. 5, no. 2, pp. 128-137, February 1987, doi: 10.1109/JSAC.1987.1146527.

## Slide 13
I. Channel Estimation
II. RIS-Aided
III. TRICE
IV. Conclusion
IV. Conclusion
Simulation: